## Slide 1
Løvholt F1, Harbitz CB1, Griffin J2, Davies G2, Cummins P2, Lorito S3, Selva J3, Basili R3, Baptista MA4, Babeyko A5, Geist E6, Parsons T6, Thio HK7, Leveque R8, Power W9, Burbidge D9, Müeller C9, Horspool N9, Yalciner A10, Kanoglu U10, Suppasri A11, Imamura F11, Aguirre Ayerbe I14, Gonzalez-Riancho14, Gonzalez M14, Wei Y8,15, Titov V15, von Hildebrandt-Andrade C16, Macias J17, Gonzalez-Vida JM17, Gailler A18, Necmioglu O19, Lynett P20, Paris R21, Cardona O22, Bernal G23 et al*
A Global Tsunami Model (GTM) network for increased understanding of tsunami hazard and risk
Main characteristics of the global tsunami hazard
1NGI, 2Geoscience Australia, 3INGV, 4IPMA, 5GFZ Potzdam, 6USGS, 7AECOM, 8Univ Washington, 9GNS, 10METU, 11IRIDES, 14Univ Cantabria, 15NOAA, 16NOAA-CTWP, 17Univ Malaga, 18CEA, 19KOERI, 20USC, 21CNRS, 22INGENIAR, 23CIMNE *+other organisations expressing interest
Dominated by earthquakes sources (about 80%). Other important sources are landslides and volcanoes.
Although tsunamis propagate far – most damage (fatality and building damage) occurs near the source.
The 50 most destructive historical tsunamis events caused 97% of all lives lost. In recent history, the 2004 Indian Ocean and 2011 Tohoku tsunamis dominate
The infrequent tsunamis involving return periods of several hundreds to thousands of years dominate losses and challenge risk modelers
The source (earthquake) statistics are poorly constrained at these return periods
This makes the evaluation and communication of uncertainties as an important part of tsunami risk assessment
Abstract: The 2004 Indian Ocean and 2011 Tohoku tsunamis highlighted the need for a thorough understanding of the risk posed by relatively infrequent but disastrous tsunamis. The latest Global Assessment Report (GAR15) resulted in fully global probabilistic tsunami hazard and risk maps, briefly presented here. Still, this complex assessment needs improvements based on the state-of-the-art research, e.g. in the treatment of uncertainty or inclusion of non-seismic tsunami sources, and in vulnerability and risk assessment. Towards implementing the Sendai Framework of Disaster Risk Reduction (SFDRR), further efforts are needed, requiring interdisciplinary expertise. We are therefore establishing a Global Tsunami Model (GTM) with the aim of i) a better understanding of tsunami hazard and risk analysis on a global scale and ii) providing a portfolio of validated tools for tsunami hazard and risk assessment at different scales.
Global tsunami hazard and risk analysis and mapping based on GAR15
GTM - towards integrating, standardizing, and harmonizing work on tsunami hazard and risk
A joint network of tsunami scientists working on probabilistic tsunami hazard and risk
Proposed initiative from the tsunami community based on GAR – (ToR in preparation)
Interested collaborators represents almost 30 organisations across the globe
A preliminary webpage is under construction (http://www.globaltsunamimodel.org)
Contribute to the implementation of the SFDRR – in particular towards Priority 1 – Understanding risk
Bring a new generation of global hazard and risk maps based on the previous GAR15 work (below)
Understand the factors driving risk
Promote standards and validated tools for tsunami hazard and risk assessment
Capacity building to practitioners and stakeholders
A broader involvement of the global tsunami community yields better understanding of tsunami risk
Methods: Probabilistic tsunami hazard and risk assessment (PTHA and PTRA)
Sources: Large earthquakes (magnitudes exceeding 7.8)
Hazard quantification: Probability for the tsunami run-up height or flow depth to exceed a threshold value
Quantifying the tsunami risk as probability of losses: Combining global exposure datasets, physical vulnerability curves and hazard maps
Large uncertainties related to: Source recurrence, exposure and inundation, vulnerability etc.  Hence global maps should be used with caution, and only for global and regional assessments
Relative probable maximum loss, PML (loss/national exposed value) map for a return period of 1500 years (Løvholt et al. in press, INGENIAR and CIMNE, 2015). The largest PML’s occur for small islands (not visible)
Global tsunami hazard map (due to earthquakes) for a return period of 2500 years (Davies et al. submitted), showing the mean run-up values.
What is GTM?
Why GTM?
GTM General Objectives
Harmonize efforts and products – GTM endorsement
Develop standardized and open source tools, guidelines and practices
Validate methods
Provide results on global and regional scales to become a term of reference for local hazard and risk analysis
Facilitate integration of results and tools from related organizations such as the Global Earthquake Model (GEM) and Global Volcano Model (GVM)
Dissemination and geo-ethics
GTM preliminary Scientific Objectives
(working group established – white paper in preparation)
Seismic sources: probability and modeling, both subduction zone and crustal earthquakes
Non-Seismic sources: landslides and volcanoes, probability and modeling
Tsunami modeling
Development of methods and numerical tools
Empirical and numerical Probabilistic Tsunami Hazard Assessment
Vulnerability and fragility
Probabilistic Tsunami Risk Assessment
References
Løvholt F, Griffin J, and Salgado-Galvez M (in press), Tsunami hazard and risk assessment at a global scale, Encylopedia of Complexity and System Science, Springer
Davies G, Griffin J, Løvholt F, Glimsdal S, Harbitz CB, Thio HK, Lorito S, Basili R, Selva J, Geist E, and Baptista MA (submitted), A global probabilistic tsunami hazard assessment, Proceedings of Arthur Holmes Meeting, Geological Society of London
  INGENIAR & CIMNE (2015). Update on the Probabilistic Modelling of Natural Risks at Global Level: Global Risk Model. Background paper prepared for the Global Assessment Report on Disaster Risk Reduction 2015.